Proiect Proiectare cu Microprocesoare
Ghiorghioiu Denisa
Grupa 30234

Sistem automat de irigatie a unei plante

Acest proiect are ca scop realizarea unui sistem automat de irigare care monitorizează nivelul de umiditate al solului și pornește sau oprește o pompă de apă în funcție de necesitățile plantei. Sistemul oferă feedback vizual și textual prin intermediul LED-urilor și al unui ecran LCD cu I2C.
### Componente utilizate
1. Pompa de apă: Este utilizată pentru a furniza apă către plante atunci când nivelul de umiditate este scăzut.
2. Releu: Controlează alimentarea pompei de apă, acționând ca un comutator controlat electronic.
3. LED-uri:
  1. LED verde: indică faptul că pompa este activă (în funcțiune).
  2. LED roșu: indică faptul că pompa este oprită.
4. Ecran LCD cu I2C: Afișează starea sistemului (nivelul de umiditate, starea pompei).
5. Senzor de umiditate: Monitorizează nivelul de umiditate al solului și transmite datele către microcontroler.
6. Fire de conexiune: Asigură conectarea componentelor electrice.
7. Microcontroler (ex. Arduino Uno): prelucrează datele de la senzor și controlează pompa, LED-urile și afișajul.
Functionalitate componente
Senzorul de umiditate
- Rol: Detectează nivelul de umiditate din sol și trimite un semnal analog către microcontroler.
- Funcționare: Dacă umiditatea scade sub un prag prestabilit, senzorul va semnaliza microcontrolerului să pornească pompa.
Pompa și releul
- Rolul pompei: Umezește solul prin pomparea apei dintr-un rezervor.
- Rolul releului: Controlează pornirea/oprirea pompei. Este activat de un semnal digital de la microcontroler.
Mod de utilizare:
      Se pune senzorul de temperatura in ghiveciul plantei, iar daca solul este uscat, pompa va porni. Pompa se va opri cand o sa detecteze umiditate.
- #include <LiquidCrystal_I2C.h>
- #include <Wire.h>
- LiquidCrystal_I2C lcd(0x27, 16, 2); // LCD with I2C address 0x27, 16 columns, 2 rows
- // Define the analog input pin for the rain sensor
- int sensorPin = A1;  // Use analog pin A1
- int val = 0;          // Variable to store sensor value
- int humidity_percent = 0;
- // Define a threshold value (you can adjust this based on testing)
- int threshold = 500;  // Set the threshold value (for example, 500)
- // Define LED pins
- int pumpOnLedPin = 7;  // LED that lights up when the pump is on
- int pumpOffLedPin = 8; // LED that lights up when the pump is off
- bool isStarted = false;  // Flag to track if "Rain sensor" has been shown
- void setup() {
- lcd.init();         // Initialize the LCD
- lcd.backlight();    // Turn on the backlight
- Serial.begin(9600); // Start the serial communication
- pinMode(6, OUTPUT); // Relay pin
- pinMode(pumpOnLedPin, OUTPUT);  // LED pin for pump on
- pinMode(pumpOffLedPin, OUTPUT); // LED pin for pump off
- digitalWrite(6, HIGH); // Set the relay to LOW (off) initially
- digitalWrite(pumpOnLedPin, LOW);  // Ensure the pump on LED is initially off
- digitalWrite(pumpOffLedPin, HIGH); // Ensure the pump off LED is initially off
- }
- void loop() {
- // Read the sensor value from the analog pin (range 0 to 1023)
- val = analogRead(sensorPin);
- // Print the sensor value to the serial monitor for debugging
- Serial.println(val);
- // Calculate humidity percentage (0 - 1023 -> 100% to 0%)
- humidity_percent = (1 - (float(val) / 1023.0)) * 100;
- if (!isStarted) {
- // Display "Rain sensor" only once at the start
- lcd.setCursor(0, 0);
- lcd.print("Rain sensor");
- delay(3000); // Wait for 3 seconds to show the message
- lcd.clear(); // Clear the LCD
- isStarted = true; // Set the flag to true so that "Rain sensor" doesn't show again
- }
- // Update the LCD with pump status and humidity percentage
- if (val <= threshold) {
- lcd.setCursor(0, 0);
- lcd.print("Pump off!"); // Display when it rains
- lcd.setCursor(0, 1);
- lcd.print(humidity_percent); // Display the humidity percentage
- lcd.print("%");
- digitalWrite(6, HIGH);  // Turn on the relay (rain detected)
- digitalWrite(pumpOnLedPin, LOW);  // Turn on the "pump on" LED
- digitalWrite(pumpOffLedPin, HIGH);  // Turn off the "pump off" LED
- //digitalWrite(7, LOW); // Optional: Turn off the buzzer
- } else {
- lcd.setCursor(0, 0);
- lcd.print("Pump on!"); // Display when there's no rain
- lcd.setCursor(0, 1);
- lcd.print(humidity_percent); // Display the humidity percentage
- lcd.print("%");
- digitalWrite(6, LOW);   // Turn off the relay (no rain)
- digitalWrite(pumpOnLedPin, HIGH);  // Turn off the "pump on" LED
- digitalWrite(pumpOffLedPin, LOW); // Turn on the "pump off" LED
- //digitalWrite(7, HIGH); // Optional: Turn on the buzzer
- }
- delay(1000); // Wait for 1 second before checking again
- }